## Slide 1
Gregory B. Jaczko
Former Chairman U.S. Nuclear Regulatory Commission
INRAG Study – “Risks of lifetime extensions of old nuclear power plants”, April 26, Online
Nuclear Plant Life Extensions in the US

## Slide 2: Overview of Talk
Reason for License Renewals in the US
Process and Status of Initial License Renewals
Subsequent License Renewal Process

## Slide 3: Reason for License Renewal in the US
Status of Existing Reactors
US law allows nulcear plant licenses for 40 years with unlimited 20 year extensions
Average age of nuclear reactors in the US is 39 years
From a peak in 2012 of 104 reactors, there are now 94 operating reactors
Many reactors uprated power to increase generation despite retirements between 2014 and 2018, but nuclear generation is decling in the US

## Slide 4: Reason for License Renewal in the US
Status of Existing Reactors
Safety problems and economic factors are driving the change
  Several plants closed for safety reasons: San Onofre, Crystal River, Fort Calhoun
  Most plants closed due to economic reasons
    Nuclear plants O&M costs are about $30/MWh as of 2019
    NEW Solar and wind are on average about $31/MWh WITHOUT subsidies
    NEW Solar is less than $30/MWh with subsidies
    NEW combined cycle gas is about $34/MWh

## Slide 6: Reason for License Renewal in the US
Status of New Reactors
In the early 2010s, the Nuclear Regulatory Commission had 18 applications for 30 new reactors – most not pursued
In 2012, the Nuclear Regulatory Commission licensed 4 new reactors by companies who planned to build them
  2 at VC Summer in South Carolina
    Canceled in 2017
  2 at Vogtle in Georgia
    Still underconstruction, but over budget by $15 billion and > 5 years behind schedule
No other plans for construction of large light water reactors
Some advanced reactors under consideration, but not immediate

## Slide 7: Reason for License Renewal in the US
Nuclear Power in the US for the next decades depends primarily on extending the operation of existing reactors
Chart: 

## Slide 8: Reason for License Renewal in the US
Ever since the NRC began considering license renewal in the late 1990s the industry and Congressional supporters have pressured the agency to adopt streamlined license renewal programs
License renewal in the US is more about preserving the operation of nuclear reactors than ensuring up-to-date safety for reactors

## Slide 9: Initial License Renewal
In 1995, the NRC adopted a new regulation to cover license extensions
The regulations adopts a process based on the two principles
  Existing regulations and processes are sufficient to maintain safety EXCEPT for new phonemena related to the aging of passive systems
  Plants must continue to update their current licensing basis throughout the license extension period
An updated environment impact review must be completed
  Primarily accomlished through a generic environmental review applicable to all facilities
This is NOT a de novo review of the safety of the facility
Standard rules about “backfitting“ apply

## Slide 10: Initial License Renewal
Features of License Renewal
Plants may request license renewals up to 20 years before the termination of their license
  For initial license renewal this means there is at least 20 years of plant operating experience – IMPORTANT for Subsequent License Renewal
License renewal reviews take 2 years or less
Plants may operate during license renewal review if they file their license in a timely manner (at least 5 years before license termination)
Nearly all plants have or will complete a 20 license extension

## Slide 11: Initial License Renewal
Ageing Management Reviews
The key feature of the license renewal process is a program to manage ageing primarily of PASSIVE components such as concrete structures, piping systems, wiring etc
  Active components were captured through maintenance programs
Each plant must identify passive systems, structures and components that could be susceptible to ageing related impacts
Each plant must then analyze the impacts of ageing beyond 40 years for these components and show either
  That the updated analysis no longer shows ageing impacts within 60 years OR
  That the ageing impacts will be monitored to ensure safe operation
    This is the basis for the license renewal review by the NRC
The NRC maintains a Generic Ageing Lesson Learned (GALL) report which reviews successful ageing management programs and expects later license renewal applicants to use the successful programs

## Slide 12: Initial License Renewal
Examples of Technical Issues Identified
Buried piping –
  Examples of buried piping systems leaking after long term ageing effects
  Identified after the fact
Concrete Degradation
Electrical Cable Submergence
  Electrical system reviews and inspections enhanced
License Renewal simply examines programs to address these issues if they are found
As more issues are identified the GALL is updated to reflect new issue areas and new programs, but license is not denied

## Slide 13: Initial License Renewal
Missed Opportunities
Plants entering license renewal are at least 40 years old with designs that are about 50 years old
Advances in materials, electronics and safety are not addressed by license renewal
  Assume the plant was safe so it will continue to be safe with additional monitoring of ageing systems

## Slide 14: Initial License Renewal
Missed Opportunities
Digital Control Rooms
  Significant safety and operational advantages of digital control review
    Current control rooms in most plants are a mixture of digital and analog components and systems
    Safety related control systems are still primarily analog
  Digital upgrades are expensive and time consuming and plants have been reluctant to move forward with modifications
  An active license renewal process could require upgrading control rooms

## Slide 15: Initial License Renewal
Missed Opportunities
Post 9/11 Security Enhancements
The primary requirement for post 9/11 security enhancements is not a system included in ageing management programs
There is no additional requirement to protect against aircraft impact by design for existing reactors (does apply to new reactors)
Backfit and cost benefit dictate many safety enhancements so normal procedures do not capture these trends

## Slide 16: Subsequent License Renewal
With continued pressure to maintain existing reactors, because few new reactors will be built and continued pressure to reduce costs, there is strong pressure to make a second license renewal as simple a process – Subsequent License Renewal
In the mid 2010, NRC staff were reluctant to have such a passive approach to license renewal. Passive components were expected to push the boundaries of safety margins in 60+ years of operations
  Pressure vessel embrittlement
  Large concrete structures

## Slide 17: Subsequent License Renewal
The weaknesses of the initial license renewal approach appear less risk significant because
  Many plants pursued license renewal before the plants had operatored close to their initial 40 year analyzed, licensed lifetime so future ageing problems may not yet have manifested
  20 years of additional operation is more easily seen as within the design margin of the original plant designs
Subsequent license extension becomes more risk significant

## Slide 18: Subsequent License Renewal
In 2014, the NRC proposed updating license renewal regulations to address some of these concerns with the new process
  Timely renewal could not happen without an ageing management program in place for new issues
  Submittalls had to be made closer to license termination to ensure there was enough information to understand ageing phenomena – currently can propose as soon as previous license extension period starts
  Post Fukushima and post 9/11 security measures should be included in ageing management programs
  Degradation monitoring programs must be maintained and reported, they are not currenlty included in operating programs
Commission rejected updating regulations

## Slide 19: Subsequent License Renewal
  Status of Subsequent License Renewals
  Reviews completed in less than two years
  Four units have had their licenses renewed a second time
    Turkey Point issued 13,14 years before subsequent license will start
    Peach Bottom also issued 13,14 years before subsequent license will start
  11 more applications are under review or expected
  Industry survey shows about half of existing plants will seek a subsequent license renewal
  License renewal does not require operation, many plants may never operate that long, but the process is so simple many will do it to preserve options

## Slide 20: Conclusion
License Renewal in the US is a pro forma step designed primarily to ensure the continued operation of nuclear reactors
The approach relies on the integrity of existing oversight programs to maintain safety
Misses opportunities to upgrade plants to modern standards using more effective systems like digital control systems
Susequent license renewals have an even weaker safety basis than initial license renewals