## Slide 1
Dr Paul Dorfman
UCL Energy Institute, University College London
INRAG Study – “Risks of lifetime extensions of old nuclear power plants”, April 26, Online
UK Ageing Reactor PLEX

## Slide 2: UK Hunterston B 965 MW AGR Nuclear Power Plant
Operation start: 1976.
Original operational life-span: 35 years, with planned closure in 2011.
Closure date extended by Office of Nuclear Regulation (ONR) at EDF’s request to 2023.
Hunterston B is now 45 years old, and constructed pre 9/11 and pre-Fukushima.
Key external risks not considered in design-base include: Reactor and spent fuel pond vulnerability, esp. plane crash potential (i.e. military and loaded large civil).

## Slide 3: Hunterston B has a history of technical problems
Insulation Degradation, Graphite Oxidation, Boiler Spine Cracking, Boiler Superheating Cracking, and Graphite Cracking.
Most significant risk is graphite cracking of the core moderator.
Not only are there significant uncertainties over the structural integrity and residual strength of Hunterston Bs graphite moderator core but also cracking in the boiler spines were identified in 2014.
Deterioration of heat exchangers, located in concrete around the reactor pressure vessel, and of the graphite core are the two key life-limiting factors for all UK AGRs.

## Slide 4: Keyway Route Cracking
Seven graphite keyways have cracks at Hunterston B.
Keyway route cracking is a very specific form of cracking, forming in pairs opposite each other, potentially splitting the graphic bricks in two.
Keyway cracks risk the core becoming misaligned, with fuel modules getting stuck in the core.
If this happens, the fuel temperature could rise and could undergo a melt.
Once radiation gets into the gas stream and the reactor vents because it’s over-pressurised, then radiation release to the atmosphere follows.

## Slide 5: ONR doubles crack limit
2015, EDF declared cracks in three of the graphite bricks in one of the Hunterston B reactors.
By 2018 over 350 cracks had been detected - an unexpectedly large increase over the previous 77 cracks identified in 2017.
Many more than EDF’s modelling predicted, and breaching its operating safety limit.
EDF requested UK Office for Nuclear Regulation (ONR) to relax the crack limit to allow the reactor to restart, proposing permission to run with up to 1,000 cracks.
Controversially, ONR accepted EDF’s revised safety case, doubling the cracks limit it had previously set.

## Slide 6: ONR: EDF’s Safety Analysis ‘Inherantly subjective’
EDF will now shut down Hunterston B nuclear power plant early - decommissioning to begin in January 2022.
In the interim, EDF has secured approval to restart one of Hunterston’s reactors for an initial six-month period (following a two-year shutdown).
However, even according to EDF, running the ageing nuclear reactor for another year could cause cracks in its core to rise by 65%.
But even that large number of significant cracks won’t breach the reactor’s operating limit for cracks - because the limit has been increased four-fold by EDF and agreed by the ONR, the UK regulators.
Despite ONR describing EDF’s safety analysis as ‘inherently subjective’ – and that EDF’s methodology for demonstrating that the reactor is safe is ‘approaching its limit of viability.’

## Slide 7: 1,331 cracks
Latest estimates put the number of cracks in August 2020 at 570 and predict that this could rise to 781 after six months operation and 943 after a year - which, according to EDF, would not exceed the currently established damage tolerance level of 1,331 cracks.
Nearly all of Britain’s nuclear fleet is composed of advanced gas-cooled reactors.
A factor of ageing in that type of reactor is cracks in the graphite bricks.
The cause of this damage is not fully understood.
One of the reasons is that there are currently limited means of detecting hidden, but developing, sub-surface cracks - so it is entirely possible that this form of age-related damage may be much more extensive.

## Slide 8: ONR: ‘Hunterston B is generally representative of the other stations.’
The graphite cores of Hunterston B, and possibly all 14 UK AGR reactors, have developed and continue to develop significant structural damage to graphite bricks including keyway cracks in the fuelled section of the reactor.
UK nuclear regulator Office for Nuclear Regulation (ONR): ‘Hunterston B is generally representative of the other stations.’
Given weight loss in graphite blocks and graphite cracking occurs in all UK AGRs; the Hunterston B example has significant implications across the entire UK AGR fleet.

## Slide 9: Estimated decommissioning costs
The UK’s civil nuclear sites including Hunterston B Power Station estimated to cost UK taxpayers around £132 billion to decommission.
Decommissiong will not be completed for another 120 years - according to a UK parliamentary Public Accountability Committee (PAC) 2019 report.